## Slide 1: DSD Final MIPS G3
B07901010 范詠為
B07901013 林子軒
B07901019 吳隆暉

## Slide 2: Outline
Baseline & Hazard handling
Branch prediction
L2 Cache

## Slide 3: Baseline & Hazard Handling

## Slide 4: Baseline AT

## Slide 5
Chart: 
| 3.5 | 5 | 5.0999999999999996 | 5.2 | 5.5 | 6
AT | 4910912350.0795 | 4516199938.9155 | 4327220107.2795 | 4733649487.4251 | 5099786196.5176 | 4568551164.1977

## Slide 6: Forwarding Unit
Alu forwarding
Register file forwarding
Write data

## Slide 7: Forwarding Unit
Branch forwarding
-> Beq, Bne, Jr, Jalr
Since we move branch and jr determination from MEM to ID for fewer flush cycle, we needs to handle this.

## Slide 8: Hazard Control
Data Hazard
-> load-use : stall 1 cycle
Data Hazard for branch
-> Beq, Bne, Jr, Jalr
-> Ex type: stall 1 cycle
-> Mem type: stall 2 cycle
Branch Hazard
-> flush 1 cycle

## Slide 9: Extension

## Slide 10: Branch Prediction
Structure
1-bit/2-bit Global Branch Predictor
1-bit/2-bit Local Branch Predictor
(m, n)-Correlated Branch Predictor
Experiment

## Slide 11: Structure - No BrPred(as NT)
Correct -> no penalty
Wrong -> 1 cycle penalty
Branch, J, Jal, Jr, Jalr are all calculated in ID stage

## Slide 12: Structure - with BrPred
Only misprediction and jump reg instructions will have 1 cycle penalty.
mispred
Jr

## Slide 13: Global Branch Predictor (testbench)
All branch instructions use one global state
1-bits/2-bits

## Slide 14: 1-bit/2-bit Local Branch Predictor
Branch History Table (BHT)
-> 128*2bit (assume big enough)
Add/Sub 1 to change state

## Slide 15: (m, n)-Correlated Branch Predictor
m : 2^m global state
n : n-bits predictor
Maintain a global state
Each branch instruction has m local n-bits predictors.

## Slide 16: (m, n)-Correlated Branch Predictor
Global state = 2b’00 means consecutive two branch not takens.
Record correlation between 3 (i.e. m+1) branches.
1st, 2nd: NT -> 3rd:T

## Slide 17: Experiment
Nested for loop

## Slide 18: Experiment
Outer = 400
Inner = 16/8/4/2
Correlated predictor is the best

## Slide 19: Experiment
More (ongoing…)
Correlated
Global/Local

## Slide 20: L2 Cache
Encountered Troubles
Structure
FSM Design
Experiment & Observation

## Slide 21: Encountered troubles
Originally, many next state logics are used in the cache design in HW3.
We hadn’t finished MIPS CHIP
So I finished many caches without thinking and testing
But pipeline MIPS needs fast response from memory
Disaster
Spent a lot of time adjusting the architecture and debugging
Lesson learnt: Better test and code simultaneously
And I suck so mush…

## Slide 22: Structure
Based on separate L2 cache structure
Focus on performance with different combination of cache mapping
We want to check the connection of miss rate and associativity
L1 cache (256 words): Direct-mapped, 2 way set-associative
L2 cache (32 words): Direct-mapped, 2/4/8 way set-associative
L1_Dcache
L2_Dcache
L1_Icache
L2_Icache
Slow Memory

## Slide 23: FSM
Writeback cache

## Slide 24: FSM

## Slide 25: FSM
Reduce several times of access memory
Proportional to total size of the cache

## Slide 26: FSM: set-associative
Replacement policy(LRU)
Non valid set
Clean set
Least Recently used set
Numeric order
Set determination of 2 way set-associative

## Slide 27: Experiment
Little difference under the original testbench due to the separate L2 cache design.
Possible reason: the miss ratio is low from the testbench itself
L1 | dm |  |  |  | 2way |  |  | 
L2 | dm | 2way | 4way | 8way | dm | 2way | 4way | 8way
L1 miss rate | 0.0521 |  |  |  | 0.1013 |  |  | 
L2 miss rate | 0.3279 |  |  |  | 0.0160 |  |  | 

## Slide 28: Experiment
Based on read-write-read test from HW3
Chart: Operation finish time
| DM | 2way | 4way | 8way
DM | 87125 | 83605 | 81845 | 98245
2way | 79445 | 75925 | 74165 | 73285
Observation:
Using more sets is not necessarily helpful.
Especially when the associativity of L2 grows overly larger than that of L1.

## Slide 29: Further Research
More experiment:
Branch predictor
L2 cache
Discuss different cache size
Use other testbenches with strong locality